## Slide 1: “Field to Finish” Working with AutoCAD Civil 3D
Shawn Herring
Civil Applications Engineer @ ProSoft, Inc
Training & Support Manager

## Slide 2: Introduction:
Shawn Herring
    9 years in Civil Engineering Community
    Drafter/Designer
    CADD Manger
    Project Manager
    Civil Engineer
    3+ Years with Autodesk Reseller
    Teach and Support Civil 3D, Map 3D, SSA and AutoCAD
    Civil 3D Certified Professional Since 2007
    Speak at numerous User Groups across the country
    Manage Support/Training Staff
    Multiple Social Media Sites
Jason Jenkins, PLS
Jason is a Professional Land Surveyor, Licensed in the State of Utah. He has 19 years’ experience in surveying and land planning, with a strong background in Civil Engineering. He was the Chief Designer and CAD Manager for an engineering firm for 9 years and has owned his own surveying firm for the last 10 years. Jason is the most recent addition to the ProSoft staff and will be a valuable asset to the civil engineering and surveying community.

## Slide 3: ▪ Follow us on any of these media sites ▪ Facebook – ProSoft Twitter - @ProSoft_AEC YouTube – ProSoftCAD http://www.youtube.com/user/ProSoftCAD LinkedIn Blog – ProSoftAEC http://prosoftaec.blogspot.com/

## Slide 4: Agenda
“Field to Finish”
Figure Prefix Database
Linework Code Set
Data Collection
Editing Survey Figures
Bonus Information
Questions

## Slide 5: Agenda
2:15 – 3:30 (Field)
Overview of Field Collection
Survey Parking Lot!!
3:30 – 4:00
Break
4:00 – 5:30 (Finish)
Create Civil 3D Setup
Import Database
Inspect and Finish!!

## Slide 6: Goals:
Learn the components and procedures required to collect linework in the field.
Witness a workflow that will work with any survey data collection equipment.
Learn how to quickly and easily edit survey figures
Understand the business benefits of collecting field data in a way that line work is created automatically.
Let’s Get Started….
At the end of today’s session…

## Slide 7: Linework Code Set
Coding Method
  Before or After
  Point Description
Ex: B TBC
  TBC B

## Slide 8: Linework Code Set
  Special Codes (Most Used)
  Begin and End linework
  Start and Stop Horizontal and Vertical Offsets

## Slide 9: Linework Code Set
  Line Segment Instructions

## Slide 10: Linework Code Set
  Curve Segment Instructions

## Slide 11: Linework Code Set
  Any Code is Customizable!
  Ex: B for Begin
  + for Begin
  E for End
  - For End
Universal Field to Finish

## Slide 12: New Linework Code Set – Universal F2F
TBC1 B
Lines (figures) are automatically created by connecting point descriptions if a linework code is used.

## Slide 13: New Linework Code Set – Universal F2F
TBC1 B
CL B
In this example B is added to the descriptions to begin linework (figures).

## Slide 14: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B

## Slide 15: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2

## Slide 16: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2
TBC2
Figures are automatically created by connecting point descriptions if a linework code is used.

## Slide 17: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2
CL
TBC2

## Slide 18: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2
CL
TBC2
CL

## Slide 19: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2
CL
TBC1
TBC2
CL

## Slide 20: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2
CL
TBC1
TBC2
CL
TBC1

## Slide 21: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2
CL
TBC1
TBC1 E
TBC2
CL
TBC1

## Slide 22: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2
CL
TBC1
TBC1 E
TBC2
CL
TBC1

## Slide 23: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2
CL
TBC1
TBC1 E
CL E
TBC2
CL
TBC1

## Slide 24: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2
CL
TBC1
TBC1 E
CL E
TBC2
CL
TBC1

## Slide 25: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2
CL
TBC1
TBC1 E
CL E
TBC2 E
TBC2
CL
TBC1

## Slide 26: New Linework Code Set – Universal F2F
TBC1 B
CL B
TBC2 B
TBC2
CL
TBC1
TBC1 E
CL E
TBC2 E
TBC2
CL
TBC1
Three figures were automatically created.

## Slide 27: Field Demo – Parking Lot

## Slide 28: Demonstration
Linework Code Set
Figure Prefix Database
Setup Civil 3D/Prepare to Import

## Slide 29: Linework Code Set
  Any Code is Customizable!
  Ex: B for Begin
  + for Begin
  E for End
  - For End
Universal Field to Finish

## Slide 30: Figure Prefix Database
Figure Prefix
Notes: Here we’ll see a simple example of a typical project scenario. With the Projects and Data Management solution that Civil 3D offers, a Vault server that can be installed on a network or local machine is where the “project” resides. We have multiple users using multiple drawings accessing and using data in the project.
We have user one who has referenced a surface from the project, and is working with it in a drawing on their machine. At the same time, we have a second user which is also referencing the same surface, but in this case is designing an alignment and profile from it. A third user is accessing the same data, but in this case, they are running an analysis on the surface. Note that these users can have read-write access to the data, allowing for a true multi-user system for sharing and managing our critical project information in real-time.

## Slide 31: Demonstration
“FINISH”
Edit and Queries
Surface creation

## Slide 32: Survey Database Files:
Import Events
Networks
Figures
Survey Points
Equipment
Figure Prefix
  Survey Database
  Equipment Database
  Figure Prefix Database
Notes: Here we’ll see a simple example of a typical project scenario. With the Projects and Data Management solution that Civil 3D offers, a Vault server that can be installed on a network or local machine is where the “project” resides. We have multiple users using multiple drawings accessing and using data in the project.
We have user one who has referenced a surface from the project, and is working with it in a drawing on their machine. At the same time, we have a second user which is also referencing the same surface, but in this case is designing an alignment and profile from it. A third user is accessing the same data, but in this case, they are running an analysis on the surface. Note that these users can have read-write access to the data, allowing for a true multi-user system for sharing and managing our critical project information in real-time.

## Slide 33: Survey Database:
Import Events Who, What, When…
Networks An Event in the Field
Figures Linework
Survey Points
Import Events
Networks
Figures
Survey Points

## Slide 34: Survey Database:
TXT
.DWG Points
Notes: Here we’ll see a simple example of a typical project scenario. With the Projects and Data Management solution that Civil 3D offers, a Vault server that can be installed on a network or local machine is where the “project” resides. We have multiple users using multiple drawings accessing and using data in the project.
We have user one who has referenced a surface from the project, and is working with it in a drawing on their machine. At the same time, we have a second user which is also referencing the same surface, but in this case is designing an alignment and profile from it. A third user is accessing the same data, but in this case, they are running an analysis on the surface. Note that these users can have read-write access to the data, allowing for a true multi-user system for sharing and managing our critical project information in real-time.

## Slide 35: Demonstration
Process Field Data
Simulate Data Collection
Lines, Curves, Double Coding…

## Slide 36: Editing Survey Figures:
Survey Point Properties
Survey Figure Properties
Resolve Crossing Breaklines

## Slide 37: Demonstration
Survey Point Editing
Survey Figure Editing
Resolve Crossing Breaklines

## Slide 38: Demonstration
Working With Notes
Survey Database Log
Survey Database Queries

## Slide 39: New Survey Query
Points and Figures
Dynamic Surface Creation

## Slide 40: New Survey Tools
Access to Field-Collected
Survey Data
Import
Label
Query

## Slide 41: Bonus Information:
Working with “Notes”
Database Log

## Slide 42: Mapcheck Tool / Curve Calculator Survey Link DC / Geodetic Calculator / COGO Geometry Editor

## Slide 43: Summary:
Learn the components and procedures required to collect linework in the field.
Witness a workflow that will work with any survey data collection equipment.
Learn how to quickly and easily edit survey figures
Understand the business benefits of collecting field data in a way that line work is created automatically.

## Slide 45
Thank you!!
For further information contact us at:
ProSoft, Inc
sherring@prosoftnet.com 888.263.0393
www.prosoftnet.com
And remember to follow us at any of the below!!